## Slide 1: MIMO (802.11n) & Next Generation 802.11n
Some slides adapted from: Dina Katabi, Kate Lin, Shyam Gollakota

## Slide 2: MIMO
Multiple-input and multiple output (MIMO) is a method for multiplying the capacity of a radio link using multiple transmit and receive antennas
h12
h11
h21
h22
x1
x2
y1
y2

## Slide 3: MIMO gains
Multiplexing gain: send more packets at the same time
Diversity gain: Increase SNR by sending packet along multiple streams

## Slide 4: Receive Diversity
How Can we Decode?
y1=h1 x1+n1
h2
h1
y2=h2 x1+n2
1- Should We Sum?
2- Should We Decode Separately?
x1

## Slide 5: Transmit Diversity
Pre-code the transmissions
h2
h1
x1
x1
y1=h1 x1+h2 x1+n1
Might add up destructively!
α
β

## Slide 6: MU-MIMO (Multi-User MIMO)
h12
h11
h21
h22
y1
y2
x1
x2
Can’t decode because Rx1 and Rx2 are separate
Solution: Interference Nulling

## Slide 7: What if we have a two-antenna receiver?
h12
h11
h21
h22
y1
y2
x1
x2
Solution: Interference Nulling

## Slide 8: Next Generation 802.11n
Notes: Today I’m going to present is about MIMO as a first-class citizen in 802.11.
The traditional 802.11 protocol was designed for single-antenna systems.
When MIMO emerges, it’s just an add-on.
However, if we rethink 802.11 design for MIMO, we can get a much higher throughput.

## Slide 9
Wireless nodes increasingly have heterogeneous numbers of antennas
1-antenna devices
2-antenna devices
3-antenna devices
Notes: MIMO technologies are emerging, and we are having more and more antennas in a single device.
But, on the other hand, there are still many devices limited by their physical size, so they can only support a single antenna.
There are also some in the middle.
So, what we see today is that wireless devices increasingly have heterogeneous numbers of antennas and different mimo capabilities.

## Slide 10: 802.11 Was Designed for 1-Antenna Nodes
When a single-antenna node transmits,
multi-antenna nodes refrain from transmitting
Alice
Bob
Chris
Notes: However, 802.11 was originally designed for single-antenna devices.
In today’s 802.11, when a single-antenna node transmits, all mimo nodes refrain from transmitting.

## Slide 11: But, MIMO Nodes Can Receive Multiple Concurrent Streams
Alice
Bob
Chris
Notes: This is however undesirable because, in principle, mimo nodes should be able to receive multiple packets concurrently.
For example, Bob’s receiver has two antennas, so should be able to receive two concurrent packets.
Given that Alice is only transmitting one packet on the medium, Bob can actually transmit another packet to his receiver.
Similarly, Chris’s receiver has three antennas, so, supposedly, can get another packet from Chris, in the presence of two ongoing transmissions.
Ok, great, we have concurrent transmissions.

## Slide 12: It’s Not That Simple
Alice
But, how do we transmit without interfering at receivers with fewer antennas?
Interference!!
Interference!!
Bob
Chris
Notes: But how about Alice’s receiver?
Alice’s receiver only has one antenna, so he can only decode one packet.
If Bob just transmits, he is gonna interfere with Alice’s receiver.
Similarly, if Chris just transmits, both Alice’s and Bob’s receivers will get hurt.
So, the question is how can we transmit concurrently, but without interfering with any existing transmissions?

## Slide 13: Enable concurrent transmissions
without harming ongoing transmissions
Goal
802.11n+
Notes: Our goal is to have concurrent transmissions across mimo nodes,
But without harming all ongoing transmissions.
In this talk, I’m going to introduce 802.11n+

## Slide 14: 802.11n+
Enables 802.11 nodes to contend for both time and concurrent transmissions
Maintains random access
Notes: N+ is the first protocol that allows mimo nodes to join ongoing transmissions without interfering with them.
Not only this, but also it maintains all the great properties of random access, which is the main reason why we love today’s 802.11 because it allows us to access the medium in a fully distributed way.
Finally, n+ is implemented, and shown in practice to improve the throughput.

## Slide 15
How to transmit without interfering with receivers with fewer antennas?
  Interference nulling
  Interference alignment
How do we achieve it in a random access manner?
  Multi-dimensional carrier sense
Notes: To achieve our goal, we will need to answer two questions.
How to transmit concurrently?
And how to do it in random access?

## Slide 16
How to transmit without interfering with receivers with fewer antennas?
  Interference nulling
  Interference alignment
How do we achieve it in a random access manner?
  Multi-dimensional carrier sense
Notes: Let’s start by answering our first question.
How can we transmit without introducing interference?

## Slide 17: Interference Nulling
Alice
Bob
nulling
Signals cancel each other at Alice’s receiver
Signals don’t cancel each other at Bob’s receiver
  Because channels are different
Notes: The answer to that is interference nulling.
So, how does it work?
Say Alice is already transmitting a packet.
And Bob wants to transmit a concurrent packet y to his receiver.
To ensure not to interfere with Alice’s receiver, Bob can null his signal at Alice’s receiver.

## Slide 18: Interference Nulling
Signals cancel each other at Alice’s receiver
Signals don’t cancel each other at Bob’s receiver
  Because channels are different
Bob’s sender learns channels either by feedback from Alice’s receiver or via reciprocity
Alice
Bob
Notes: In particular, he can use his first antenna to transmit his packet y multiplied by some given variable alpha.
The signal goes through a channel h1.
Then, Alice’s receiver will see an interference h1ay from Bob.
Bob can use the other antenna to transmit by
Then, the signal goes through a different channel h2.
So, now Alice’s receiver will get an interference, which is the summation of these two signals from Bob.
Nulling the signal means that we want to force this interference to be 0, which is doable.
Regardless of the channel values, we can always pick some alpha beta to satisfy this constraint such that two signals will sum up to 0 at Alice’s receiver.
Then, Alice’s receiver will not see any signal from Bob.
So, this is how nulling works.
But, one thing worth to notice is that such nulling doesn’t prevent Bob’s receiver from receiving his signal.
This is because the channels received by Bob’s receiver are different from h1 and h2, Cancelling signals for Alice’s receiver doesn’t mean that cancelling signals for Bob’s receiver.
That’s why Bob can transmit a packet to his receiver.

## Slide 19: Interference Nulling
Interference Nulling
Q: How to transmit without interfering with receivers with fewer antennas?
A: Nulling
Alice
Bob
Notes: So far, we have an answer to our question.
To transmit without interfering with ongoing transmission, we can use nulling and now we know how to null the signals.
But are we done?

## Slide 20
Alice
Bob
Chris
Notes: What if we have more mimo nodes, like Chris, who also wants to transmit concurrently

## Slide 21: Is Nulling Alone Enough? NO!!
Alice
Bob
Chris
NO!
Notes: Can we just use nulling to allow Chris to transmit without interfering with either Alice’s receiver or Bob’s receiver?
Unfortunately, the answer is no.
Turns out that when we want to support more concurrent transmissions, nulling alone is not enough.
For example, if Chris wants to transmit concurrently, he should not interfere with both Alice’s receiver and Bob’s receiver.

## Slide 22: Is Nulling Alone Enough? NO!!
Alice
Bob
Chris
NO!
Chris needs to null at three antennas
Notes: To do that, Chris will need to cancel his signals for three antennas, one at Alice’s receiver and two at Bob’s receiver.
The bad news is it is not doable.
This is because a 3-antenna transmitter cannot null his signals at 3 receive antennas.
Let’s see why.

## Slide 23: Is Nulling Alone Enough? NO!!
Alice
Bob
Chris
Transmit Nothing!!!
NO!
null
Are we doomed?
No, we can use interference alignment
Notes: If Chris wants to transmit a packet z, as before, he can transmit a weight version of the signal z.
We can write the nulling equations.
We will have one equation for each antenna we want to null the signal, which should be set to 0.
We don’t need to worry about these equations, because the details are not so important.
The important thing is that the only solution for these equation is to set all variables to 0, which means that Chris is not transmitting at all.
Clearly, this solution is clearly not what we want, because this means that Chris cannot transmit anything to his receiver.
This is why nulling doesn’t work.
But, are we doomed? Is there any way to get three concurrent transmissions?
The reason why nulling is not doable is because making your signal invisible is a very strong constraint.
But, does Chris really need to make his signals invisible for every receiver?
Fortunately, no!
I’m going to show you that Chris doesn’t really need to cancel his signals for both Alice’s receiver and Bob’s receiver.
In fact, Chris can use a new technique, called interference alignment, to transmit his packet.
Let me explain to you how interference alignment works.

## Slide 24: MIMO Basics
N-antenna node receives in N-dimensional space
antenna 1
antenna 2
antenna 1
antenna 1
antenna 2
antenna 3
Notes: To understand what is alignment, I will need to introduce to you some very important properties of MIMO.
The first thing we need to know is that an n-antenna node receives in n-dimensional space.
What does that mean?
If I have a single-antenna receiver, I receives signals at only one antenna, so I receive signals in one-dimension.
But, if I have two antennas, I will receive the signal at the first antennas, and also receive the signal at the second antenna.
So really I’m receiving a vector in a two-dimensional space.
Similarly, a three-antenna node receives at each antenna a different signal, so the received signal is a vector in a three-dimensional space.
We can even generalize it to an n-antenna node, which will receive in n-dimensional space.

## Slide 25: MIMO Basics
N-antenna node receives in N-dimensional space
N-antenna receiver can decode N signals
2-antenna receiver
y1
y2
Notes: The second thing we need to know is that the transmitter can rotate the received signal to whatever direction he wants.
For example, if someone is transmitting a signal, then this 2-antenna receiver receives a vector y in his two-dimensional space.
Say we want to rotate the received signal to y’.
We can easily do that.
First thing to note is that we can always write y’ as Ry, where R is a rotation matrix.
So, to rotate the received signal y to y’, all the transmitter has to do is to multiply its transmitted signal by the same rotation matrix R.
So, now we can rotate the signal to a new direction y’.

## Slide 26: MIMO Basics
N-antenna node receives in N-dimensional space
N-antenna receiver can decode N signals
Transmitter can rotate the received signal
y’
y
2-antenna receiver
= Ry
Rotate by multiplying transmitted signal by a rotation matrix R
Notes: The second thing we need to know is that the transmitter can rotate the received signal to whatever direction he wants.
For example, if someone is transmitting a signal, then this 2-antenna receiver receives a vector y in his two-dimensional space.
Say we want to rotate the received signal to y’.
We can easily do that.
First thing to note is that we can always write y’ as Ry, where R is a rotation matrix.
So, to rotate the received signal y to y’, all the transmitter has to do is to multiply its transmitted signal by the same rotation matrix R.
So, now we can rotate the signal to a new direction y’.

## Slide 27: Interference Alignment
wanted signal
I1
I2
If I1 and I2 are aligned,
 appear as one interferer
 2-antenna receiver can decode the wanted signal
2-antenna receiver
Notes: With this basic understanding about mimo, next, let me use a very simple example to explain what is interference alignment.
Let’s consider a 2-antenna node who is receiving one signal he wants and another signal he doesn’t want.
Because he has two antennas, he can decode these two signals to get the signal he wants.
But, say that we have the second interferer.
Now this two-antenna receiver cannot decode these three signals in his two-dimensional space.
So, he cannot get the signal he wants.
But If this new interferer can somehow align his signal along the direction of the first interferer by rotating his signal,

## Slide 28: Interference Alignment
If I1 and I2 are aligned,
 appear as one interferer
 2-antenna receiver can decode the wanted signal
2-antenna receiver
I1 + I2
wanted signal
Notes: , this receiver will see only one interference.
Then, it looks like there are only two signals on the medium, so he can still decode two signals.
One is the signal he wants, the other is the sum of two interferences he doesn’t want.
Ok, now we know how to align the signal.

## Slide 29: Use Nulling and Alignment
aligning
nulling
Alice (unwanted)
Bob
Chris
Alice
Bob
Chris
Null as before
Notes: Ok, let’s go back to see why this alignment is a very nice property for solving our problem.
Remember that Chris doesn’t want to interfere with both Alice’s receiver and Bob’s receiver.
For Alice’s receiver, Chris can still use nulling to cancel his signal. That’s fine.
However, for Bob’s receiver, we are going to use this new concept: interference alignment.
What we do is to leverage the fact that Bob’s receiver is already receiving some signals from Alice,
But he doesn’t want that signal.
So it doesn’t hurt to put another interference on top of Alice’s signal.
Basically, Chris doesn’t really need to completely cancel his signal for Bob’s receiver.
All he has to do is to align his signal with Alice’s signal.

## Slide 30: Use Nulling and Alignment
aligning
Alice
Bob
Chris
nulling
Alice + Chris (unwanted)
Bob
2-signals in 2D-space
Can decode Bob’s signal
Notes: As a results, from the perspective of Bob’s receiver, it looks like there are still only two signals, one is Bob’s signal, the other is this garbage signal, which is the combination of Alice and Chris.
So, he can still decode these two signals.
Even though he can not decode Alice’s and Chris’s signal individually, but it doesn’t matter because he doesn’t want these two signals.
The important thing is that he can get what he wants, which is Bob’s signal.
Ok, we’ve shown that we can use nulling and alignment to transmit three concurrent packets.
Therefore, n+ allows all senders to transmit, but the throughput will be as high as if only the three-antenna sender is transmitting all the time.
And this is the maximum throughput we can get for this topology.
Of course, there are more details about how to fully implement interference nulling and interference alignment, and these are described in the paper.
The thing I want to emphasize is that we can do the same process for any generic scenario.
Specifically, in our paper,

## Slide 31: Use Nulling and Alignment
Alice
Bob
Chris
3 packets through receivers have fewer than 3 antennas
Notes: What if we have more mimo nodes, like Chris, who also wants to transmit concurrently

## Slide 32: MAC Protocol
Each sender computes in a distributed way
  where and how to null
  where and how to align
Analytically proved:
  # concurrent streams = # max antenna per sender
Notes: we have a general protocol, which allows each sender to compute where and how to null, also where and how to align in a distributed way.
We also proved that the number of concurrent streams can be equal to the maximum number of antennas supported by any sender.

## Slide 33
How to transmit without interfering with ongoing transmissions?
  Interference nulling
  Interference alignment
How do we achieve it in a random access manner?
  Multi-dimensional carrier sense
Notes: So, we achieve our goal.
Now, we know how to use the combination of nulling and alignment of transmit concurrently.

## Slide 34
How to transmit without interfering with receivers with fewer antennas?
  Interference nulling
  Interference alignment
How do we achieve it in a random access manner?
  Multi-dimensional carrier sense
Notes: But, the second question is can we achieve this goal without loosing random access?

## Slide 35
In 802.11, contend using carrier sense
Multi-Dimensional Carrier Sense
But, how to contend despite ongoing transmissions?
Notes: In 802.11, random access works because it allows us to use carrier sense to contend for the medium in a fully distributed way.
However, carrier sense doesn’t work for concurrent transmissions.
Because we cannot just check whether the medium is idle or not.
Otherwise, we are not going to have concurrent transmissions across different nodes.
So, what we need is to extend carrier sense to work despite ongoing transmissions.
But how can we do that?
Our solution is multidimensional carrier sense.

## Slide 36
Alice
Bob
Alice
Alice
one signal
Alice
Bob
two signals
Say that Ben is performing carrier sense
Ben
Distinguishable using simple linear algebra
Notes: Consider a two-antenna node Ben who is interested in concurrent transmissions.
Ben needs to distinguish between the following two scenarios.
There is only one transmissions on the medium, or
There are two transmissions on the medium.
Because if there is only one transmission on the medium, he has two antennas, so he can sneak out another packet.
But if there are already two transmissions, he should not transmit.
As I said earlier, because Ben has two antennas, he receives in a two-dimensional space.
So, what he wants is to distinguish between this scenario where there is only one vector from Alice’s transmission, and the second scenario where there are two vectors from Alice and Bob.
This is a simple linear algebra problem that we can solve using say Gaussian elimination.
So, let’s see how can we use this concept in the protocol.

## Slide 37: Multi-Dimensional Carrier Sense
Alice
Bob
Contend
Ben
Alice
Contend
Alice
Bob and Ben contend for a second concurrent transmission
Notes: Let’s use the same example where Alice is transmitting.
All the nodes that have more than 1 antenna, like Bob and Ben, transmit concurrently with Alice.
So, they need to contend with each other, but how can they contend in the presence of Alice’s signal?
As I said, Bob and Ben both have two antennas, so they both see Alice’s signal in a two-dimensional space.

## Slide 38: Multi-Dimensional Carrier Sense
Alice
Bob
Ben
Alice
Project orthogonal to Alice’s signal
Alice
Contend
Contend
Notes: Given this mimo property, the basic idea of our multi-dimensional carrier sense is that Bob and Ben can both project orthogonal to Alice’s signal.

## Slide 39: Multi-Dimensional Carrier Sense
Alice
Bob
Contend
orthogonal to Alice
no signal from Alice!!
Alice
orthogonal to Alice
no signal from Alice!!
Ben
Alice
Contend
Project orthogonal to Alice’s signal
Notes: In particular, they can both project the signal along a direction orthogonal to Alice’s signal.
After projection, they will not see Alice’s signal, so the medium looks idle.

## Slide 40: Multi-Dimensional Carrier Sense
Alice
Bob
Alice
Apply carrier sense in the orthogonal space
Ben
Alice
orthogonal to Alice
no signal from Alice!!
orthogonal to Alice
no signal from Alice!!
Contend
Contend
Notes: Therefore, they can simply apply standard 802.11 carrier sense.

## Slide 41: Multi-Dimensional Carrier Sense
Alice
Alice
Bob
Bob
Detect energy after projection
Win
Lose
Ben
Notes: They both listen to the medium after projection.
One of them will win the contention and transmit first, say Bob.
Now, Ben starts seeing some signals from Bob.
Then, after projection, he will detect energy in this orthogonal direction, and can identify that there are two transmissions now.
Because he only has two antennas, he knows that he lost the contention, and should not transmit.
Effectively, we’ve extended carrier sense to work despite ongoing transmissions.
Here we use two-antenna nodes to explain our protocol, but everything works for arbitrary number of antennas.

## Slide 42: Multi-Dimensional Carrier Sense
To contend for the next concurrent transmission
Project orthogonal to ongoing signals
Apply standard carrier sense

## Slide 43
How to transmit without interfering with receivers with fewer antennas?
  Interference nulling
  Interference alignment
How do we achieve it in a random access manner?
  Multi-dimensional carrier sense
Notes: So what we have now is a protocol, which allows us to transmit concurrently, but at the same time, maintain the random access nature by using multi-dimensional carrier sense.