## Slide 1
NETWORK CONNECTIVITY FOR IOT
HARI BALAKRISHNAN
Mobile and Sensor Computing
Spring 2016

## Slide 2: networking: “GLUE” for the IOt
IoT’s “technology push” from the convergence of
  Embedded computing
  Sensing & actuation
  Wireless networks

## Slide 3: The iot connectivity soup

## Slide 4: networking: “GLUE” for the IOt
(Too) many different approaches, (too) many different standards, (too) much confusion
One size does not fit all: best network depends on application
What are the key organizing principles and ideas?

## Slide 5: Architecture, simplified
“Things” (devices, sensors, actuators)
data
Mobile Gateways (phones, tablets)
Gateways
Internet
Servers in the “cloud”
Mediate & Translate
Notes: Gateways are “edge” devices that translate and mediate between the wireless network of “things” and the Internet

## Slide 6: But, in fact, a rich design space
How should gateways and things communicate?
Many answers, many approaches

## Slide 7: Can’t we just use the wireless internet?
  Cellular and Wi-Fi
Yes, we can…
  except when we can’t!

## Slide 8: Wireless internet for iot?
Cellular (LTE/4G, 3G, 2G) and Wi-Fi are
  + Widely available
  + High bandwidth (for most purposes), so can support high-rate apps
  But, each has two big drawbacks
  High power: not suitable for battery-operated scenarios
  Cellular: often high cost (esp. per byte if usage-per-thing is low)
  Wi-Fi: OK in most buildings, but not for longer range
  Wi-Fi: In-building powered things (speakers, washers, refrigerators, …)
  Cellular: High-valued powered things (e.g., “connected car”)

## Slide 9: Cellular power consumption
Deng & Balakrishnan, “Traffic-Aware Techniques to Reduce 3G/LTE Energy Consumption,” CoNext 2012.
Power monitor apparatus
IDLE
IDLE
DATA
High-power IDLE

## Slide 10: Iot network design space
Device-to-gateway range
inches
body/room
factory/campus
building
miles
Device’s data rate (“duty cycle”)
Gbytes per day
bytes per day
Wi-Fi: hours, Gbytes/day, factory
LTE: hours--, Gbytes/day, miles
Battery life (low-power operation)
hours
20 years
powered

## Slide 11: Why so many iot networks?
Because engineers love inventing technologies!
But really because you can pick many interesting regions from this design space
Device-to-gateway range
inches
body/room
factory/campus
building
miles
Battery life (low-power operation)
hours
20 years
Device’s data rate (“duty cycle”)
10s of Mbits/s
bytes per day

## Slide 12: Why so many iot networks?
Because engineers love inventing technologies!
But really because you can pick many interesting regions from this design space
  Note, axes aren’t independent
  And technology evolves fast
Device-to-gateway range
inches
body/room
factory/campus
building
miles
Battery life (low-power operation)
hours
20 years
Device’s data rate (“duty cycle”)
10s of Mbits/s
bytes per day

## Slide 13: Why so many iot networks?
Because engineers love inventing technologies!
But really because you can pick many interesting regions from this design space
  Note, axes aren’t independent
  And technology evolves fast
  And bundling into popular devices speeds-up adoption, changing the economics
    Cf. Wi-Fi  laptops (without external cards)
    Bluetooth classic  cell phones  wireless headsets
    Bluetooth Low Energy (BLE)  iPhone then Android smartphones  “body/room” with months-to-years at low duty cycles
Device-to-gateway range
inches
body/room
factory/campus
building
miles
Battery life (low-power operation)
hours
20 years
Device’s data rate (“duty cycle”)
10s of Mbits/s
bytes per day

## Slide 14: BODY/Room-AREA example: BlE
Device-to-gateway range
body/room 10 meters typical 50 meters under good conditions with high TX Longer range might not always be good
Device’s data rate (“duty cycle”)
peak: ~100s of kbits/s
Battery life (low-power operation)
Months-to-years if ~100s kbytes per day
Started as “Wibree” by Nokia (2006)
Dominant technology today
Because of smartphones
Smartphones as gateways
Wearables, fitness trackers Vehicles (bikes, cars)

## Slide 15: How does ble work?
Two parts:
  Advertisements (aka “beaconing”) for device discovery
  Connection phase to exchange data
Peripheral: device with data
Central: gateway
PERIPHERAL
PERIPHERAL
CENTRAL

## Slide 16: BLE Advertisements are periodic
Typical period: 100 ms (“iBeacon”)
Less frequent is fine
Triggered advertisements are often a good idea
Trade-off between energy consumed and discovery latency

## Slide 17: On connection
DEVICE (PERIPHERAL)
SERVICE 1
SERVICE 2
SERVICE 3
CHARACTERISTIC 1a
CHARACTERISTIC 1b
CHARACTERISTIC 2a
CHARACTERISTIC 2b
CHARACTERISTIC 2c
CHARACTERISTIC 3a
READABLE
READ/WRITE NOTIFICATIONS
Usually support
OTA (over-the-air upgrades)

## Slide 18: ON CONNECTION: MAC PROTOCOL
Central orchestrates data communication
Key idea: time-schedule to reduce energy consumption
On connect: exchange parameters
Frequency hopping sequence
Connection interval, i.e., periodicity of data exchange (T milliseconds)
Every T milliseconds, Central and Peripheral exchange up to 4 packets, alternating turns
Then Peripheral can go back to sleep until next interval

## Slide 19: Battery lifetime calculation
Consider an IoT system with coin-cell battery-powered nodes
Battery: 250 mAh (milliamp-hours) capacity; 3 Volts
Recall that power = voltage * current and energy = power * time
So this battery has 0.75 amp-hour-volts = 0.75*3600 Joules = 2.7 kJ of energy
Example of BLE current draw:
Standby: 1 microAmp (typically in the 1-10 microAmp range)
Receive (RX): 3.3 mA
Transmit (TX): 4 mA
Suppose device transmits every second: how long does the battery last?

## Slide 20: Battery calculation (CONT.)
Consider an IoT system with coin-cell battery-powered nodes
Battery: 250 mAh (milliamp-hours) capacity; 3 Volts
Recall that power = voltage * current and energy = power * time
So this battery has 0.75 amp-hour-volts = 0.75*3600 Joules = 2.7 kJ of energy
Example of BLE current draw:
Standby: 1 microAmp (typically in the 1-10 microAmp range)
Receive (RX): 3.3 mA
Transmit (TX): 4 mA
Suppose device transmits every second: how long does the battery last?
1 microAmp
4 mA for 1 millisecond
Why 1 millisecond?
125 bytes @1 Mbit/s

## Slide 21: Battery calculation (Cont.)
Ramp-up and down: 1 milliAmp for 5 milliseconds
Over a 1 second interval, average current is:
4 microAmps (xmit) + 5 microAmps (ramping) + 1 microAmp (standby)
= 10 microAmps
Therefore, battery lifetime
= 250 mAh / 10 microAmps
= 250 mAh / 0.01 mA
= 25,000 hours
= 2 years and 10 months
This works because it’s sleeping most of the time!
1 microAmp
4 milliAmp for 1 millisecond
Why 1 millisecond?
125 bytes @1 Mbit/s

## Slide 22: IoT “Gateway problem” paper

## Slide 23: extending communication range
Device-to-gateway range
inches
body/room
factory/ campus
building
miles
Battery life (low-power operation)
hours
20 years
Device’s data rate (“duty cycle”)
Gbytes per day
bytes per day

## Slide 24: EXTENDING RANGE: MESH NETWORKS
1980s: DARPA packet radio networks
1990s: mobile ad hoc networks (MANET)

## Slide 25: Extending range: mesh networks
Late 90s, 2000s: Sensor networks
2000s: Mesh networks for Internet

## Slide 26: Extending range: mesh networks
2010s: Mesh networks for IoT
Zigbee
6LoWPAN: IPv6 over low-power wireless personal area networks
Both (typically) run over the 802.15.4 MAC standard
Routing protocol with different metrics, such as “expected transmission time”
Use case: devices communicating with gateway across multiple hops
Node duty cycles higher, some nodes do much more work
http://processors.wiki.ti.com/index.php/Contiki-6LOWPAN (Creative commons)

## Slide 27: Wireless Mesh routing
Each link delivers a packet with some probability
What path should be used for a packet?
Gateway
75%
100%
100%
Gateway
75%
50%
100%
75%
ETX: Expected Transmission Count
(expected tx time if link rate fixed)
On single link = 1 / Probability of packet delivery
Add for each link on path and pick smallest

## Slide 28: Even longer range (city-scale)
Device-to-gateway range
inches
body/room
factory/ campus
building
miles
Battery life (low-power operation)
hours
20 years
Device’s data rate (“duty cycle”)
Gbytes per day
bytes per day

## Slide 29: When the internet is miles away
Use mobile devices
as data mules
Trade-off: delay
Delay-tolerant network (DTN)

## Slide 30: What if we want long range and low delay?
“Long-range IoT networks”
Examples: Sigfox, LoRaWAN, cellular IoT proposals (narrowband LTE, etc.)
Low-power designs (months to years of battery life)
Low or ultra-low throughput (a few bytes per day to achieve long-enough battery life at a rate of a few kbps)
Networks like LoRaWAN also include localization capabilities

## Slide 31: What if we want long range and low delay
Second choice: Cellular (of course!)
Examples: LTE/4G, 3G, etc.
High-power consumption, so only when power isn’t an issue
Delay still a concern for data-intensive, latency-sensitive applications

## Slide 32: Continuous recognition apps
Face Recognition
Augmented Reality Shopping
Augmented Reality Tourist App
Driver Assistance
SLOW

## Slide 33: Glimpse: continuous real-time recognition
Continuous, real-time object recognition on mobile devices in a video stream
Continuously identify and locate objects in each frame
Alice
Bob
Alice
Bob
Bob
Alice
Alice
The Internet of Things
T. Chen, L. Ravindranath, S. Deng, P. Bahl, H. Balakrishnan, SenSys 2015

## Slide 34: Recognition pipeline
Detection
Feature Extraction
Classification
Stop Sign
T. Chen, L. Ravindranath, S. Deng, P. Bahl, H. Balakrishnan, SenSys 2015

## Slide 35: Recognition pipeline
Detection
Feature Extraction
Classification
Stop Sign
Computationally expensive and memory-intensive
  Server is hundreds of times faster than embedded/mobile computer
  Scaling to large number of images requires servers

## Slide 36: Solution: server offload
Server
Client
Detection
Feature Extraction
Classification
Labels,
bounding boxes
Frame
Camera
Display
Network
Two big challenges
End-to-end latency lowers object recognition accuracy
2. Bandwidth and battery-efficiency

## Slide 37: IDEA: Device-side active cache
Cache and run tracking through the cached frames
Server
Frame 0
Active Cache
Network

## Slide 38
Server
Alice
Frame 0
Active Cache
Network

## Slide 39
Server
Alice
Active Cache
Frame 0
Frame 30
Run tracking from Frame 0 to Frame 30
Network

## Slide 40: Performance on faces
Average end-to-end frame delay to server and back: 430 ms

## Slide 41: Performance on road signs
Average end-to-end frame delay to server and back: 520 ms

## Slide 42: What have we learned?
Rich design space for things-gateway communication
Gateways
Things
Servers
Internet
Device-to-gateway range
inches
body/room
factory/campus
building
miles
Battery life (low-power operation)
hours
20 years
Device’s data rate (“duty cycle”)
10s of Mbits/s
bytes per day
Think along three dimensions:
data rate/duty cycle
battery
range
Three case studies
Low-power design (Bluetooth LE): advertisement, time-scheduled MAC
Range extension techniques: muling & meshing (Zigbee, 6LoWPAN)
Data-intensive IoT: continuous recognition

## Slide 43: Open questions and future work
We are not even at the end of the beginning of IoT!
(Who wants to turn on a light bulb by going to an app?!)
What if you want city-scale, high-rate, low-power sensing? (e.g., high-fidelity vibration, weather, image sensors)
Current systems gated by standby power (microWatts)
Recent advances have shown nanoWatt standby power
How will this change IoT networks?
Current IoT apps are “siloed” from each other How to integrate them?

## Slide 44: DE-Siloing
Today: build IoT devices/sensors, build an app, build a cloud service
Vertically-integrated: hard to integrate and slows innovation Gateway functions are repeatedly invented
The issue: real value is in the data, not in the devices!
Possible (non-exclusive) approaches
Coordinate access to data via server-side APIs in the cloud
Provide access to data in smartphone apps via “kits” (HomeKit, Healthkit, Google Fit, …)
Develop a generic gateway (multiple technologies)

## Slide 45: predictions
Shake-up in standards: multiple winners, but they will divide up the “three-dimensional space”
Ultra-low power IoT systems and networks
Compute-intensive (data-intensive) IoT systems and networks
De-siloed architectures
Smartphone-centric v. hidden (ubiquitous) computing
Notes: Anticipate changes and innovations in the coming years