## Slide 1: extending communication range
Device-to-gateway range
inches
body/room
factory/ campus
building
miles
Battery life (low-power operation)
hours
20 years
Device’s data rate (“duty cycle”)
Gbytes per day
bytes per day

## Slide 2: EXTENDING RANGE: MESH NETWORKS
1980s: DARPA packet radio networks
1990s: mobile ad hoc networks (MANET)

## Slide 3: Extending range: mesh networks
Late 90s, 2000s: Sensor networks
2000s: Mesh networks for Internet

## Slide 4: Extending range: mesh networks
2010s: Mesh networks for IoT
Zigbee
6LoWPAN: IPv6 over low-power wireless personal area networks
Both (typically) run over the 802.15.4 MAC standard
Routing protocol with different metrics, such as “expected transmission time”
Use case: devices communicating with gateway across multiple hops
Node duty cycles higher, some nodes do much more work
http://processors.wiki.ti.com/index.php/Contiki-6LOWPAN (Creative commons)

## Slide 5: A High-Throughput Path Metric for Multi-Hop Wireless Routing
Douglas S. J. De Couto
Daniel Aguayo, John Bicket, and Robert Morris
Notes: [Probably cut?] Today I’m going to talk about some technical problems in building multihop wireless networks, and I’m going to present a new routing metric that helps routing protocols find high-throughput routes.

## Slide 6: Indoor wireless network TESTBED
5th floor
6th floor
29 devices with 802.11b radios (fixed transmit power) in ‘ad hoc’ mode
4th floor
3rd floor
2nd floor
Notes: We wanted to experiment with routing protocols, so we built an indoor testbed. The indoor testbed has many practical advantages for experimentation: ease of administration, upgrading, accessibility --- every node has a wired link for control. The rest of this talk will talk about results from the indoor network.
The indoor net is like a Roofnet, but inside: commodity PCs & 802.11 hardware, omnidirectional antennas. Although not identical, results on the indoor network should be indicative of the Roofnet.
Looking at all the previous work on ad hoc protocols, it seemed as if it should be easy to get any of those protocols to work on a small static network. We started by implementing DSDV.

## Slide 7: Testbed UDP throughput WITH HOP-COUNT
better
Better
Notes: Unfortunately, the result was disappointing. We had poor latency for remote logins over the wireless network, and file transfers were slow. Since at one point we used the wireless network for control as well as experimentation, network performance problems were clear.
To be more precise about the problems, we ran UDP throughput tests. This figure shows CDF of UDP throughputs between 100 pairs of nodes using DSDV with min hopcount.
X-axis is pkts/sec; Y-axis is fraction of pairs that got less than that many pkts/sec
Example: 50% of pairs sent less than 100 pkts/sec
Lower right is better.
Max 802.11 throughput at this bit-rate and packet size is 451 pkts/sec, so some pairs are doing pretty well.
But 20% of pairs had ~0 throughput!
Clearly, those zeros are not great; but what would the right result look like? Is the network disconnected, for example?

## Slide 8: What throughput is possible?
‘Best’ for each pair is highest measured throughput of 10 promising static routes
Routing protocol
‘Best’
Notes: Yes, we can do better. Best beats DSDV hop-count by a large margin. So we know DSDV is not doing as well as possible. Things to notice:
Notice 1-hop/2-hop distinction at horizontal segment -- when routing multi-hop, there is some throughput reduction to be expected.
For one-hop routes, we get approximately as good as we deserve.
Difference in one-hop routes is due to DSDV protocol overhead: route broadcasts.
DSDV finds many zero-throughput routes between many pairs, even though non-zero routes exist between those pairs.
For the rest of the multi-hop routes, DSDV still finds routes with much lower throughput than is possible -- by up to a factor of 2 to 5!

## Slide 9: Throughput differs between paths
Paths from 23 to 36
Notes: Because there is such variation in the links, there is also lots of variation in paths that can be found, even for the same hop count. This is why hop-count doesn’t do as well as the best.
more hops = larger number of potential paths, more variations
Minimum hop-count chooses essentially randomly between paths, so expected hop-count throughput is much less than the best found.

## Slide 10: Challenge: more hops, less throughput
Links in network share radio spectrum
Extra hops reduce throughput
Throughput = 1/2
Throughput = 1
Throughput = 1/3
Notes: Challenge number one: on shared-channel wireless networks, successive hops of a multi-hop route will interfere with each other.
Max 2-hop throughput = 1/2 -- Middle node has to send and receive each packet once.
Max 3-hop = 1/3 -- 1st and 3rd node can’t transmit at the same time, collisions at node 2.
Effect reaches steady state after about 4 or five hops, but exact behavior depends on the interference between nodes (radio parameters, propagation conditions, etc.)

## Slide 11: Challenge: many links are lossy
Smooth link distribution complicates link classification.
One-hop broadcast delivery ratios
‘Good’
‘Bad’
Notes: Figure shows 227 non-zero (one-way) links out of 812 total.
Half of the (one-way) links deliver less than 90% of packets.
One-quarter of the links deliver less than 50% of packets.
So our routing protocol will probably find routes with a significant proportion of lossy links; it needs to be able to compare links and choose between good and bad links.
We can’t assume a bi-modal distribution and classify links as ‘good’ or ‘bad’, because wherever you place that threshold, a large number of potential links will be left on the wrong side of the threshold.
More importantly, though, sometimes the protocol will only be able to make a choice among all ‘bad’ links, or there may be many ‘good’ links -- as the distribution shows, there would still be lots of difference between links in the same category, which the protocol should take into account when choosing links. For example, choosing between a 60% link and a 40% link.
Other interesting note: hop-count will seek out marginal links: min hop-count == max distance per link.

## Slide 12: Challenge: many links are asymmetric
Many links are good in one direction, but lossy in the other
Broadcast delivery ratios in both link directions.
Very asymmetric link.
Notes: Graph shows broadcast delivery ratios in each direction for all non-zero links. Things to notice are:
Not only are many links lossy, many are asymmetric. Many of the good links are the good side of an asymmetric link.
Asymmetric links have long bars, they have very different delivery ratios in the two directions.
Asymmetric links complicate routing protocols.

## Slide 13: Effect of asymmetry on DISTANCE-VECTOR ROUTING
100%
100%
100%
8%
But, throughput of B-A = 0.08
B-C-A = 0.5
B successfully receives all of A’s route ads, and installs a one-hop route to A.
A
C
B
100%
100%
Notes: Asymmetry can hurt the performance of a distance-vector type protocol -- route advertisement will always be heard over the link from A to B, causing B to install routes to A using that link. However, Node B’s throughput to A will only be about 10% of the maximum link throughput -- it would be better to use a 2-hop route via C with 50% throughput.
Transition to next slide: so we’ve got these 3 problems (longer routes have less throughput; many links are lossy; many links are asymmetric). How can we use a route metric to find high-throughput paths in the face of these problems.

## Slide 14: A strawman route metric
Maximize bottleneck throughput
50%
Delivery ratio = 100%
51%
51%
D
A
B
C
Actual throughput:
A-B-C : ABBABBABB = 33%
A-D-C : AADDAADD = 25%
Bottleneck throughput:
A-B-C = 50%
A-D-C = 51%
Notes: Here is one metric that aims to find high throughput routes.
Unfortunately it doesn’t work for our case with shared channels and link-layer retransmissions.
Notice what happens in the actual throughput examples. On average, every other tx by A, B, or D gets lost (red splats), but they still occupy space & time, using up potential throughput.

## Slide 15: Another strawman metric
Maximize end-to-end delivery ratio
51%
100%
50%
A
B
C
Actual throughput:
A-B-C : ABBABBABB = 33%
A-C : AAAAAAAA = 50%
A-B-C = 51%
A-C = 50%
End-to-end delivery ratio:
Notes: Neither of these two metrics select the route with the highest throughput. In fact, on our sorts of network, they will make very bad choices. And what we are interested in is finding the highest throughput path.
To be fair, max bottleneck throughput would likely work well with point-to-point links, and max e2e delivery ratio would likely work well in the absence of link-layer retransmissions.

## Slide 16: New metric: ETX
Minimize total transmissions per packet
(ETX, ‘Expected Transmission Count’)
Link throughput  1/ Link ETX
Delivery Ratio
100%
50%
33%
Throughput
100%
50%
33%
Link ETX
1
2
3

## Slide 17: Calculating link ETX
Assuming link-layer acknowledgments (ACKs) and retransmissions (true in 802.11, BLE, 802.15.4, etc.):
P(TX success) = P(Data success)  P(ACK success)
Link ETX = 1 / P(TX success)
= 1 / [ P(Data success)  P(ACK success) ]
Estimating link ETX:
P(Data success)  measured fwd delivery ratio rfwd
P(ACK success)  measured rev delivery ratio rrev
Link ETX  1 / (rfwd  rrev)

## Slide 18: Measuring delivery ratios
Each node broadcasts small link probes (with Wi-Fi, this paper uses 134 bytes), once per second
Nodes remember probes received over past 10 seconds
Reverse delivery ratios estimated as
rrev  pkts received / pkts sent
Forward delivery ratios obtained from neighbors (piggybacked on probes)
There are other ways to obtain this information

## Slide 19: PATH (“ROUTE”) ETX
Route ETX
1
2
2
3
Path ETX = Sum of link ETXs
5
Throughput
100%
50%
50%
33%
20%

## Slide 20: ETX Properties
ETX predicts throughput for short routes (1, 2, and 3 hops) for wireless networks with link-layer retransmissions and a shared medium
ETX quantifies loss
ETX quantifies asymmetry
ETX quantifies throughput reduction of longer routes
Notes: Although the ETX implementation may make errors in throughput prediction, we don’t actually care about exactly predicting throughput: we want to rank routes in order of throughput. So systematic mistakes (under/over-predictions) aren’t a problem.
ETX is designed especially for link-layer ACKs; it doesn’t make any sense otherwise.

## Slide 21: ETX caveats
ETX link probes are susceptible to MAC unfairness and hidden terminals
  Route ETX measurements change under load
ETX estimates are based on measurements of a single link probe size (e.g., 134 bytes)
  Under-estimates data loss ratios, over-estimates ACK loss ratios
  But there are ways around this problem
ETX assumes all links run at one bit-rate
  Subsequent work has been done to overcome this problem, leading to “ETT”, the expected transmission time metric

## Slide 22: Evaluation Setup
Indoor network, 802.11b, ‘ad hoc’ mode
1 Mbps, 1 mW, small packets (134 bytes), RTS/CTS disabled
DSDV + modifications to respect metrics
  Packets are routed using route table snapshot to avoid route instability under load.
Also: DSR + modifications to respect metrics
(DSDV and DSR are two different routing protocols for mesh networks)
Notes: Using 1mW instead of 30mW makes the network less connected, giving longer routes and fewer very good links. However, the number of marginal links is about the same.
1 mW provides *fewer* route choices [although more practical choices, because there are fewere pairs with one-hop routes, which means more pairs are actually choosing between multi-hop routes].
DSDV is a proactive distance vector protocol; DSR is a reactive source routing protocol.

## Slide 23: ETX improves DSDV throughput
better
DSDV overhead
‘Best’
DSDV+ETX
DSDV+hop-count
Notes: Why does DSDV+ETX do better than DSDV+hop-count?
ETX avoids all of the asymmetric links (bottom left of purple line)
But even where hop-count was finding routes that work, ETX is finding better routes, because it is avoiding lossy links in general, e.g. in the middle-left of the graph.
ETX can only increase throughput for pairs that do not have 1-hop routes. Since both hop-count & ETX find the same 1-hop routes, the throughput is the same -- that’s the right side of the graph where all the lines are the same.
We notice that neither ETX nor hop-count do as well as ‘best’ for the 1-hop routes on the right -- that’s because of the DSDV overhead.
ETX provides the most benefit for pairs that are many hops away -- the more hops, the better is ETX’s advantage, because more hops means more possible routes; more possible routes means hopcount is more likely to choose a bad route.
There are still one or two zeros; these are nodes that didn’t have any good links during the experiment.
[ don’t refer to right or left -- use ‘upper right’, and ‘lower left’ ]
[ discuss ‘zeroes’ or not? ]
Avg. ETX throughput: 158 pkts/sec
Avg. hop-count throughput: 137 pkts/sec
15% improvement
Ignoring 1-hops:
ETX: 101
Hop-count: 73
38% improvement

## Slide 24: Per-pair DSDV throughputs

## Slide 25: DSR with ETX
DSR+ETX
‘Best’
DSR+hop-count
Notes: TX feedback allows DSR to switch up to a better route when a link loses packets, so even if DSR finds routes with lossy links, it can switch to a better route when packet losses occur. In this way, DSR is always improving the route quality.
However, ETX provides some benefit: it lets DSR start of with better routes, avoiding the time DSR wastes using bad routes before switching to good routes -- although we don’t know if that is the reason for the gap on this slide, or not.
Because our DSR implementation has a link cache, DSR can find and switch to a new route without even performing a route request broadcast -- it simply re-runs Dijkstra’s algorithm over the non-broken links it knows about. So new route requests are very rare. Although I can’t quantify it, so don’t talk about it.

## Slide 26: DSR with ETX (no TX feedback)
DSR+ETX
‘Best’
DSR+hop-count
Notes: Without TX feedback, DSR uses the first shortest route it finds. Adding ETX enables DSR to better select an initial route. TX feedback and route metrics can be seen as orthogonal mechanisms.
RTM says don’t talk about this, because tx feedback seemed to work pretty well in our experiments [ when would this be the case ]: For example, you might not want to switch off of a route just because of a few seconds of transmission failure -- it may still be the fastest route out there, on average.

## Slide 27: Some related work
Threshold-based techniques
  DARPA PRNet, 1970s–80s [Jubin87]: Minimum hop-count, ignore ‘bad’ links (delivery ratio  5/8 in either direction)
  Link handshaking [Lundgren02, Chin02]: Nodes exchange neighbor sets to filter out asymmetric links.
  SNR-based approaches [Hu02]: Mark low-SNR links as ‘bad’, and avoid them
Mote sensors
  Product of link delivery ratios [Yarvis02]
  Woo and Culler: Similar proposal to ETX for sensor networks (~concurrent)
Notes: Many other people have noticed the problems with poor wireless links, and many different ideas have been proposed and implemented.

## Slide 28: Summary
ETX is a new route metric for multi-hop wireless networks
ETX accounts for
  Throughput reduction of extra hops
  Lossy and asymmetric links
  Link-layer acknowledgements
ETX finds better routes!
Notes: [ ETX will be more important for bigger networks? -- finding good routes will be more important; is ETX the best way to find good routes? It doesn’t suck, anyway… ]

## Slide 29: Even longer range (city-scale)
Device-to-gateway range
inches
body/room
factory/ campus
building
miles
Battery life (low-power operation)
hours
20 years
Device’s data rate (“duty cycle”)
Gbytes per day
bytes per day

## Slide 30: When the internet is miles away
Use mobile devices
as data mules
Trade-off: delay
Delay-tolerant network (DTN)
Example we will study: Zebranet

## Slide 31: What if we want long range and low delay?
“Long-range IoT networks”
Examples: Sigfox, LoRaWAN, cellular IoT proposals (narrowband LTE, etc.)
Low-power designs (months to years of battery life)
Low or ultra-low throughput (a few bytes per day to achieve long-enough battery life at a rate of a few kbps)
Networks like LoRaWAN also include localization capabilities

## Slide 32: What if we want long range and low delay
Second choice: Cellular (of course!)
Examples: LTE/4G, 3G, etc.
High-power consumption, so only when power isn’t an issue
Delay still a concern for data-intensive, latency-sensitive applications

## Slide 33: Continuous recognition apps
Face Recognition
Augmented Reality Shopping
Augmented Reality Tourist App
Driver Assistance
SLOW

## Slide 34: Glimpse: continuous real-time recognition
Continuous, real-time object recognition on mobile devices in a video stream
Continuously identify and locate objects in each frame
Alice
Bob
Alice
Bob
Bob
Alice
Alice
We will study this paper later in the course
T. Chen, L. Ravindranath, S. Deng, P. Bahl, H. Balakrishnan, SenSys 2015

## Slide 35: Recognition pipeline
Detection
Feature Extraction
Classification
Stop Sign
T. Chen, L. Ravindranath, S. Deng, P. Bahl, H. Balakrishnan, SenSys 2015

## Slide 36: Recognition pipeline
Detection
Feature Extraction
Classification
Stop Sign
Computationally expensive and memory-intensive
  Server is hundreds of times faster than embedded/mobile computer
  Scaling to large number of images requires servers

## Slide 37: Solution: server offload
Server
Client
Detection
Feature Extraction
Classification
Labels,
bounding boxes
Frame
Camera
Display
Network
Two big challenges
End-to-end latency lowers object recognition accuracy
2. Bandwidth and battery-efficiency

## Slide 38: IDEA: Device-side active cache
Cache and run tracking through the cached frames
Server
Frame 0
Active Cache
Network

## Slide 39
Server
Alice
Frame 0
Active Cache
Network

## Slide 40
Server
Alice
Active Cache
Frame 0
Frame 30
Run tracking from Frame 0 to Frame 30
Network

## Slide 41: Performance on faces
Average end-to-end frame delay to server and back: 430 ms

## Slide 42: Performance on road signs
Average end-to-end frame delay to server and back: 520 ms

## Slide 43: SUMMARY AND PLAN
Rich design space for things-gateway communication
Gateways
Things
Servers
Internet
Device-to-gateway range
inches
body/room
factory/campus
building
miles
Battery life (low-power operation)
hours
20 years
Device’s data rate (“duty cycle”)
10s of Mbits/s
bytes per day
Think along three dimensions:
data rate/duty cycle
battery
range
Case studies
Low-power design (Bluetooth LE): advertisement, time-scheduled MAC
Range extension techniques
  Mesh networking
  Muling
In-network computing and aggregation (LEACH, TAG)
Data-intensive IoT: continuous recognition

## Slide 44: Open questions and future work
What if you want city-scale, high-rate, low-power sensing? (e.g., high-fidelity vibration, weather, image sensors)
Current systems gated by standby power (microWatts)
Recent advances have shown nanoWatt standby power
How will this change IoT networks?
Current IoT apps are “siloed” from each other How to integrate them?

## Slide 45: DE-Siloing
Today: build IoT devices/sensors, build an app, build a cloud service
Vertically-integrated: hard to integrate and slows innovation Gateway functions are repeatedly invented
The issue: real value is in the data, not in the devices!
Possible (non-exclusive) approaches
Coordinate access to data via server-side APIs in the cloud
Provide access to data in smartphone apps via “kits” (HomeKit, Healthkit, Google Fit, …)
Develop a generic gateway (multiple technologies)

## Slide 46: predictions
Shake-up in standards: multiple winners, but they will divide up the “three-dimensional space”
Ultra-low power IoT systems and networks
Compute-intensive (data-intensive) IoT systems and networks
De-siloed architectures
Smartphone-centric v. hidden (ubiquitous) computing
Notes: Anticipate changes and innovations in the coming years