## Slide 1: LEACH: An Application-Specific Protocol Architecture for Wireless Microsensor Networks
Wendi Heinzelman Anantha Chandrakasan Hari Balakrishnan
Massachusetts Institute of Technology

## Slide 2: Sensor Networks
Remote monitoring of the environment
  Surveillance
  Machine diagnostics
Relevant parameters:
  System lifetime (energy efficiency)
  Quality
  Latency
Base station
A
B
D
E
f(A-G)
C
F
G

## Slide 3: Context: MIT m-AMPS Project (1999)
Energy-optimized sensors
  Node architecture and radio hardware
  OS, algorithms, and protocols
Assumptions:
  Base station far from nodes
  All nodes energy-constrained
  Locally, data correlated
Communication protocols important
Node
RF module

## Slide 4: Prior Work
Direct transmission
  Energy scales as Rn
Routing
  E.g., Min transmission Energy
  Multi-step communication
  Short lifetimes for close nodes
Clustering
  Cellular model
  Needs high-energy cluster-head
ABC if:
dAB2+dBC2<dAC2
A
B
C
R

## Slide 5: LEACH
Low-Energy Adaptive Clustering Hierarchy
  Adaptive, self-configuring cluster formation
  Localized control for data transfers
  Low-energy medium access
  Application-specific data aggregation
Base station
Cluster-head

## Slide 6: LEACH Operation
Randomized cluster formation
  Each node decides to become cluster-head with some probability
  Picked so the expected number of cluster-heads is k
  k is a system parameter (and there’s a way to pick a good k)
Rotate cluster-heads each round
  Clusters formed during set-up
  Data transfers during steady-state
  Requires nodes to be synchronized
Time
•••
START
START
START
Set-up
Frame
Round
Steady-state

## Slide 7: Distributed Cluster Formation
r +1 = current round of operation
k = system parameter
Ci(t) = 1 if node i a CH in last r rounds
• Assumes nodes begin with equal energy
• Each node CH once in N/k rounds
Autonomous decisions lead to desirable emergent behavior

## Slide 8: Unequal Initial Energies
High-energy nodes CH more often than low-energy nodes
Ei(t) = energy of node i at time t
Etotal(t) = total energy in system at time t
  Cluster-head nodes
  Ei(t)  Eo – X
  Pi(t)  0
Non-cluster-head nodes
Ei(t)  Eo
Pi(t)  k/(N-kr)
If nodes begin with Eo
Etotal  Eo(N-kr) + (Eo-X)kr

## Slide 9: Distributed Cluster Formation Algorithm
• No global control
• Flexible, fault-tolerant
Using Pi(t)
Choose CH with highest-SNR announcement
Cluster-head
Nodes
Non-CH
Nodes

## Slide 10: Dynamic Clusters
Adaptive clusters
Rotation to evenly distribute energy load
Cluster-heads = •
Clusters during different rounds in LEACH

## Slide 11: LEACH Steady-State
Set-up
Steady-state
Cluster-head coordinates transmissions
  TDMA schedule
  Node i transmits once per frame
Low-energy approach
  No collisions
  Maximize sleep time
Clusters formed
Time
Slot for
node i
Slot for
node i
•••
Frame

## Slide 12: Inter-Cluster Interference
Transmission in different clusters can collide
  Nodes minimize transmission power
  Each cluster has unique, orthogonal spreading code (e.g., CDMA codes)
  Distributed solution to minimize interference
B
A
C
Cluster B
Cluster C

## Slide 13: LEACH Medium Access
ADV
• CSMA
• Large power, small messages
ADV
Join-REQ
SCH
Time
Steady-state
Set-up
Join-REQ
• CSMA
• Large power, small messages
SCH
• CDMA code
• Power to reach all members
CH
CH
Non-CH
Data Transfer to CH
• TDMA (with CDMA code) – no collisions
• Power to reach CH, large messages

## Slide 14: Application-Specific Data Aggregation
Local sensor data often correlated
Data aggregation
  Common signal enhanced/noise reduced
  Improved detection and classification
Compute to reduce communication energy at cluster-head
.
.
.
Data
Aggregation

## Slide 15: Simulation Parameters
Nodes | 100
Network size | 100 m x 100 m
Base station location | (50,175)
Radio prop. speed | 3x108 m/s
Processing delay | 50 ms
Radio speed | 100 kbps
Radio electronics | 50 nJ/bit
Transmit amplifier | 100 pJ/bit/m2
Beamforming cost | 5 nJ/bit/signal
Data size | 500 bytes
Base Station
75 meters
100 meters
100 meters

## Slide 16: Optimum Number of Clusters, k
N=100
M=100
75 < dtoBS < 185
 2 < k < 6
Average energy per round (J)
Number of clusters (k)
Analytic
Result:
Simulation
Result:
k=7
k=9
k=5
k=3
k=1
k=11

## Slide 17: Centralized Cluster Formation (LEACH-C)
All Nodes
Base Station
• Only nodes with Ei > mE eligible
• Simulated annealing
• Attempts to compute optimal clusters for comparison
• Needs GPS or other location-tracking method
• Small packets
• Large energy

## Slide 18: Simulations: Data Over Time (Assuming no energy constraints)
Amount of data received at BS
Time (s)
Static-
Clustering
LEACH
LEACH-C
MTE
Static clustering: no set-up time
LEACH data – 2 hops
MTE data – 10 hops on average

## Slide 19: Simulations: Data per Energy
LEACH achieves order of magnitude more messages per Joule
Data aggregation successful
Amount of data received at BS
Energy Dissipation (J)
Static-
Clustering
LEACH-C
LEACH
MTE

## Slide 20: Network Lifetime with Limited Energy
Number of nodes alive
Amount of data received at BS
Static-
Clustering
LEACH-C
LEACH
MTE
LEACH delivers over 10 times amount of data over system lifetime
Rotating cluster-heads is effective